## Slide 1: PLC Applications
Module 2
Sequential circuits and Step sequence

## Slide 2: Objectives
Analyze conditional control tasks and develop proper solutions for such tasks.
Understand and utilize relay-based safety circuit with LOGO! Controller.
Apply sequential control routines to malty-stage systems.
Develop step sequence control routines using “Pulse relay” programming block

## Slide 3: Introduction
In many applications control tasks are done in sequence.
As an example: 1. the mixing machine shown in figure . contains three units: feeder, mixer, and water circulator.
It is very important to i) start the water circulator and the ii)feeder units before starting the iii)mixer unit.
The reason for that is to avoid overloading the mixer unit.
Mixing machine

## Slide 4: 2.Pedestrian signal
Pedestrian signal
Another example is shown in figure 2.2; a pedestrian signal includes a countdown timer, which shows pedestrians how much time remains to cross the intersection. The pedestrian signal must stay red until the car signal goes red.

## Slide 5: Conditional control
In many applications control tasks are done in sequence.
A programming instruction that tells the
controller to execute part of a program only if
conditions are true is called conditional
control routine.

## Slide 6: Example for conditional control

## Slide 7
In the ladder diagram shown in figure 2.3, I1 a normally open pushbutton and I2 a normally closed pushbutton enables and disables Q1 respectively;
while I3 a normally open pushbutton and I4 a normally closed pushbuttons enables and disables Q2 respectively.
Due to that the normally open contact of Q1 is connected to the circuit of Q2 in series, Q1 becomes an AND condition for Q2.
Therefore, only when Q1 is enabled can Q2 be enabled.

## Slide 8
If the control task contains more than one condition, all conditions are to be added in series in the same rung(ladder).
The switching OFF Q1 will immediately terminate Q2.
In some applications a condition is required only to start an action then the action can be stopped alone.
In this case a latch is to be used across the condition.

## Slide 9: Latching conditional control routine

## Slide 10: Sequential control
When tasks involved in a control system are
to be done in a certain order control is said to
be sequential control.
this is very common in industrial applications,

## Slide 11: example of Sequential control [Automatic grain store]

## Slide 12
A grain store is to be controlled by LOGO!
The grain is tipped into a pit and transported from there into a cyclone by means of an elevator (conveyor belt with scoops).
The cyclone separates the corn from the chaff which is blown away.
The heavier corn drops downwards and is transported by a conveyor worm into a silo.

## Slide 13
To ensure that neither the cyclone nor the conveyor worm is overloaded, the system must be switched on as follows:
Conveyor worm  Cyclone  Elevator
The following conditions apply:
• Switching-off must be carried out in the reverse order.
• Operation is only carried out using the control panel shown in figure 2.6.
• The emergency stop button can be used any time to stop the overall system.

## Slide 14
Note : All green PBs are N.O and all red PBs are N.C
A safety circuit with EMERGENCY STOP must be provided separately

## Slide 15: Safety circuit
If the safety of a person or system is endangered, it must be possible to stop the plant safely and immediately.
The following requirements apply:
• EMERGENCY STOP must have priority over all other operations
• The state resulting in the danger must be stopped without a power supply.
• Resetting of the EMERGENCY STOP must not result in switching-on of the plant again.
• EMERGENCY STOP must be carried out using electromechanical devices.
• EMERGENCY STOP is always carried out using an NC contact.

## Slide 16: Safety circuit
The control circuit shown in figure 2.7 is a common safety circuit used in many industrial applications;
in this circuit a normally open pushbutton (N.O PB) provides a current path when it is pressed, which will energize the relay coil.
After releasing the ON PB, the relay coil stays energized because of the current path provided by the relay contact.
A normally open contact taken from the relay is connected in series with the output for safety.
This circuit can be used in our grain store example as a safety circuit

## Slide 18: the assignment list for the I/O of the grain store example
Inputs |  | 
Input | Name | Address
Start conveyor worm | S1 | I1
Stop conveyor worm | S2 | I2
Start cyclone | S3 | I3
Stop cyclone | S4 | I4
Start elevator | S5 | I5
Stop elevator | S6 | I6
Switch ON PB | S7 | Safety circuit
Emergency stop | S8 | Safety circuit
Relay coil | K1 | I9
Outputs |  | 
Output | Name | Address
Conveyor worm | M1 | Q1
Cyclone | M2 | Q2
Elevator | M3 | Q3
Conveyor lamp | P1 | Q4
Cyclone lamp | P2 | Q5
Elevator lamp | P3 | Q6

## Slide 19: Wiring diagram - grain store
This wiring diagram contains three colors of wires:
Black: wires connecting inputs.
Green: wires controlling motors.
Blue: wires connecting lamps.
Red: emergency stop circuit.

## Slide 20: First programming step – grain store

## Slide 21: modified version of the FBD with emergency stop

## Slide 22: Sequential start
Still our three stages are not in sequence.
Any stage can start at any time.
But the system requires that Q2 can only be switched on if Q1 is already switched on and Q3 cannot be switched on before Q2.
To create a sequential-start circuit, the output of the previous stage should be used as a SET input for the current stage as in figure 2.11

## Slide 24: Grain store – sequential start

## Slide 25: Sequential stop
To create a sequential-stop circuit, the output of the next stage should be used as a RESET input for the current stage as in figure

## Slide 26: Grain store
To stop the grain store stages sequentially, the output of the third stage becomes a RESET input for the second stage, and the output of the second stage becomes a RESET input for the first stage, the new FBD is shown

## Slide 27: Pulse relay programming block

## Slide 28
Pulse relay programming block has three inputs; like in the normal RS latch block input S is used to set the output Q to logic 1 and input R is used to set the output Q to logic 0.
Unlike the normal latch programming block in Pulse relay programming block there is a third input that is Trg. Input Trg is used to toggle the status of the output Q

## Slide 29
High signal at Trg changes the output from ON to OFF or from OFF to ON when both S and R are 0, however input Trg does not influence the output when S = 1 or R = 1.
Step sequence is a sequential control circuit in which one step is done every time the input is triggered.
Startup flag M8
The M8 flag is set in the first cycle of the user program and it is reset after the first program execution cycle.